## Slide 1: BMD ENG 301 Quantitative Systems Physiology (Nervous System)
Lecture 6: Neural Signals in Dendrites
2022_v2
Professor Malcolm A. MacIver

## Slide 2: Switch to Doc camera
Notes to be scanned into PDF

## Slide 3: Spinal Motor Neuron
Axon
How can we model summation of synaptic inputs?

## Slide 4: History of neural cable theory
Cable theory developed for signal flow along electrical cables in the 19th century
Original neural application by Hodgkin and Rushton (1946) to the conduction of potential along an axon
Rall (1959) extended theory and applied it to the dendritic trees of neurons.
Wilfred Rall

## Slide 5: Dendritic Cable
A. One portion of dendrite
B. divided into three sub-cylinders.
C. Discrete electrical model for the three sub-cylinders.
Notes: This figure show the modeling procedures of dendrites. Figure A shows one portion of dendrite. In Figure B, it’s divided into three sub-cylinders. Figure C is the discrete electrical model for the three sub-cylinders.

## Slide 7
Equivalent electrical circuit
Leaky insulator
Poor conductor
Cm
Rm
Ri/2
Ri/2
VLeak
OUTSIDE
INSIDE
Parallel RC Circuit
VLeak is the resting membrane potential

## Slide 8
Cable equation
2V
x2
= Ra
(V – Eleak)
+ Cm
V
t
Rm
[
]
Membrane
Resistance
Membrane
Capacitance
Internal
Resistance

## Slide 9
N.B.: ra is often used to mean axial (internal) resistance but many use ri instead
ri

## Slide 10: d/dt=0 d/dx=0
Assume conductor is a semi-infinite long cable that extends from x=0 to x=inf

## Slide 11: Signal propagation

## Slide 12
Charge Degradation over Time
2V
x2
= 0
 2V
x2
= Ri
(V – Vleak)
+ Cm
V
t
Rm
[
]
Ignore space:
So:
V = V0 exp(
-t
Rm.Cm
)
Where Rm.Cm = t = time constant

## Slide 13: Representation of time constant
V0
V
t
t
37 %

## Slide 14
Charge Degradation over Distance
V
t
= 0
2V
x2
= Ri
(V – Vleak)
+ Cm
V
t
Rm
[
]
Ignore time:
So:
V(x) = A1e(x/l) + A2e(-x/l)
Where l = length constant
l = sqroot(Rm/Ri)

## Slide 15: Representation of length constant
V0
V
x
l
37 %

## Slide 16: Equivalent Cylinder Theorem
Equivalent Cylinder Theorem: an entire class of dendritic trees can be reduced into a single equivalent cylinder if the following conditions are met:
  The values of ri and rm are the same in all branches;
  All terminals end at the same boundary condition;
  All terminal branches end at the same electrotonic distance from the origin in main branch
  The 3/2 power law at every branch point
Original tree
L11, d11
L21, d21
L22, d22
L32, d32
L31, d31
Equivalent cylinder
L, d
Notes: ri: intracellular resistance; rm: membrane resistance
Three seconds power law

## Slide 17: Rall Model

## Slide 18: Rall Model
Allowed modeling of dendritic behavior
  Confirmed by experimental results
Stimulation at different distances along arbor
Modeling of EPSPs

## Slide 19: Rall Model

## Slide 20
What if Rm is not constant, depending on x, V and t?